## Slide 1: Digital Electronics

## Slide 2: Mechatronics

## Slide 3: Digital and Analog Quantities

## Slide 4: An Analog System

## Slide 5: A System Using Digital and Analog Methods

## Slide 6: Basic Terminology
Binary Digits
Codes
Logic Levels
Digital Waveforms
Ideal Pulse
Nonideal pulse
Notes: The overshoot and ringing are sometimes produced by stray inductive and capacitive effects.
The droop can be caused by stray capacitive and circuit resistance, forming an RC circuit with a low time constant.

## Slide 7: Waveform Characteristics
?Period
?Frequency
?Duty Cycle

## Slide 8: The Clock

## Slide 9: Timing Diagrams

## Slide 10: Data Transfer

## Slide 11
Unit No. | Topics
1 | Number system, Logic gates, Boolean algebra, NAND and NOR implementation of logic functions. Determination of Boolean functions from Digital Circuits.
2 | Standard Representations of Logical Functions, SOP and POS form, Simplification of Logical functions using K-map.
3 | Combinational Logic Circuit: Adder, Subtractor, Magnitude Comparator, Code converters etc. MSI Circuits: Multiplexers, Demultiplexers, Decoders, Encoders etc.
4 | Sequential circuits: Latches and Flip-flops, Counters, Shift registers.
5 | Analysis of sequential circuits: State tables and state diagrams. Timing circuits.
6 | Introduction to logic families. Semiconductor memories, ROM, PAL, PLA and Microprocessor.

## Slide 12
Textbook
Digital Logic and Computer Design by M. Morris Mano, Prentice-Hall, 2015.
Floyd T. L., Digital Fundamentals, 10th Edition, Pearson Education, 2011.
Reference Books
Fundamental of Digital Electronics by A. Anand Kumar, 4th Edition, Prentice Hall, 2016.
Digital Principles and Applications by Malvino & Leach, 8th Edition, McGraw Hill, 2014.
Modern Digital Electronics by R. P. Jain, 4th Edition, McGraw Hill, 2009.
Digital Integrated Electronics by Paul & Schilling, McGraw Hill, 2008.
The evaluation scheme is as follows:
End Semester Examination: 50 marks
Mid Semester Examination: 30 marks
Quizzes: 2 quizzes of 10 marks each

## Slide 16: Postulates and Theorems of Boolean Algebra

## Slide 17: Draw logic diagrams to implement the following Boolean expression

## Slide 18: Write Boolean Expression

## Slide 19: Write Boolean Expression

## Slide 20: Write Boolean Expression

## Slide 21: Write Boolean Expression

## Slide 22
d
c
a
b

## Slide 23
d
c
a
b

## Slide 24
Find the complement of the expression: x′y+(x+z)(x+y′)
Find the dual of the expression: x′y+(x+z)(x+y′)

## Slide 25: Minterms and Maxterms

## Slide 26: Minterms and Maxterms
A Boolean function can be expressed algebraically from a given truth table by forming a minterm for each combination of the variables that produces a 1 in the function and then taking the OR of all those terms.
Any Boolean function can be expressed as a sum of minterms

## Slide 27: Minterms and Maxterms
Any Boolean function can be expressed as a product of maxterms.
Boolean functions expressed as a sum of minterms or product of maxterms are said to be in canonical form.

## Slide 28
Express the Boolean function F = A + B′C as a sum of minterms.

## Slide 29
Express the Boolean function F = xy + x′z as a product of maxterms.

## Slide 30: Conversion between Canonical Forms
That is, the maxterm with subscript j is a complement of the minterm with the same subscript j and vice versa.
To convert from one canonical form to another, interchange the symbols Σ and Π and list those numbers missing from the original form. In order to find the missing terms, one must realize that the total number of minterms or maxterms is , where n is the number of binary variables in the function.

## Slide 31
F = xy + x′z

## Slide 32: Standard Forms
Sum of products.
Product of Sums.

## Slide 38: Karnaugh map or K-map method
A K-map is a diagram made up of squares, with each square representing one minterm of the function that is to be minimized.
Boolean function can be expressed as a sum of minterms.
The map presents a visual diagram of all possible ways a function may be expressed in standard forms (sum of products or product of sums).
Simplest algebraic expression is one that has a minimum number of terms with the smallest possible number of literals in each term.

## Slide 40: NAND AND NOR IMPLEMENTATION
NAND Circuits

## Slide 41: Two-Level Implementation

## Slide 42: Multilevel NAND Circuits

## Slide 43: Multilevel NAND Circuits

## Slide 44: NOR Implementation

## Slide 45: NOR Implementation

## Slide 50: Combinational Circuit
Adder
Subtractor
Multiplier
Comparator
Decoder
Encoder
Multiplexer

## Slide 51
Comparator

## Slide 52: State Reduction
Reducing the number of states in a state table, while keeping the external input–output requirements unchanged.
The states themselves are of secondary importance, because we are interested only in output sequences caused by input sequences.

## Slide 53
“Two states are said to be equivalent if, for each member of the set of inputs, they give exactly the same output and send the circuit either to the same state or to an equivalent state.”

## Slide 55: State Assignment

## Slide 56: Designing synchronous sequential circuits
From the word description and specifications of the desired operation, derive a state diagram for the circuit.
Reduce the number of states if necessary.
Assign binary values to the states.
Obtain the binary-coded state table.
Choose the type of flip-flops to be used.
Derive the simplified flip-flop input equations and output equations.
Draw the logic diagram.

## Slide 58
Logic diagram of a sequence detector

## Slide 59: Excitation Tables

## Slide 60: Synthesis Using JK Flip-Flops

## Slide 62: Synthesis Using T Flip-Flops
Binary Counter

## Slide 64: Registers and Counters
A register is a collection of flip-flops used to store binary data.
Each flip-flop stores 1 bit of information.
All flip-flops share a common clock signal.
An n-bit register consists of n flip-flops → stores n bits
A counter is a special type of register.
It goes through a predefined sequence of binary states
Each state represents a count value
Up counter, Down counter, Up/Down counter

## Slide 65
Register Includes flip flop and combinational logic gates:
Flip-flops → store data
Combinational logic gates → control data flow
Flip-flops hold binary information
Logic gates determine how data is loaded, transferred, or modified.
Four-bit register with parallel load
Load = 1: New data is loaded on the next clock edge
Load = 0: Register holds its current value

## Slide 66
Four-bit shift register
0 | 1 | 0 | 1
…000111
1 | 0 | 1 | 0
…00011
1
1 | 1 | 0 | 1
…0001
01

## Slide 67: Serial Transfer
Data is processed one bit at a time using shift operations.

## Slide 68: Serial Addition

## Slide 69: Serial Addition

## Slide 70: Serial Addition

## Slide 71: Universal Shift Register
Serial in → Parallel out: Data shifted in serially can be read simultaneously from flip-flop outputs.
Parallel in → Serial out: Data loaded in parallel can be shifted out one bit at a time.
Parallel input and Parallel output.
Shift data both right and left.
Clear control: Reset register to 0
Clock input: Synchronizes operations
Shift-right control: Enables right shift + serial I/O
Shift-left control: Enables left shift + serial I/O
Parallel-load control: Enables parallel data input (n lines)
Parallel outputs: n output lines available
Hold state: Retains data (no change on clock)
Unidirectional shift register
Bidirectional shift register
Universal shift register

## Slide 80: Counters
A counter is a register that goes through a fixed sequence of states.
Triggered by input pulses (clock or external signals)
Sequence can be:
  Binary or Any custom-defined sequence
Binary Counter
Follows binary number sequence
An n-bit counter → n flip-flops
Counts from 0 to (2ⁿ − 1)
Ripple (Asynchronous) Counter
Flip-flops are triggered by outputs of other flip-flops
No common clock for all stages
Simple but slower (propagation delay)
Synchronous Counter
All flip-flops share a common clock
Operate simultaneously
Faster and more reliable

## Slide 81
UP Counter
Down Counter

## Slide 82: BCD Ripple Counter

## Slide 84: Synchronous Counters

## Slide 85: Four-bit up–down binary counter

## Slide 86: BCD Counter

## Slide 87: Counter with Unused States
Self-correcting Counter

## Slide 88: Ring Counter
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
1 | 0 | 0 | 0
A ring counter is a circular shift register with only one flip-flop being set at any particular time; all others are cleared.

## Slide 89: Generation of timing signals
: shift register with flipflops or an -bit binary counter together with an line decoder
Example: 16 timing signals
16-bit shift register connected as a ring counter
Or
4-bit binary counter and a 4-to-16-line decoder

## Slide 90: Johnson Counter
0 | 0 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
1 | 1 | 1 | 1
0 | 1 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 0 | 1
0 | 0 | 0 | 0
1 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
1 | 1 | 1 | 1
0 | 1 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 0 | 1
0 | 0 | 0 | 0
1 | 0 | 0 | 0
Number of flip-flops is less than that in a ring counter, and the decoder requires only two-input gates